## Slide 1
SMART INDIA HACKATHON 2026 · PROBLEM STATEMENT 26173 · ISRO SPACE APPLICATIONS CENTRE
Sanwad संवाद
Voice in. Text across. Voice out.
A fully offline, open-source emergency walkie-talkie for Android. Local STT + TTS in 10 Indian languages — built for the links where audio simply cannot fit.
100% ON-DEVICE
10 INDIAN LANGUAGES
OPEN SOURCE ONLY
Team: ______________________________ Team ID: ______________

## Slide 2
THE PROBLEM
When the network dies, voice is the last link
Sanwad · PS 26173 · ISRO SAC · SIH 2026
02
• Disasters take the network first. Floods, cyclones, quakes and coastal operations cut cellular exactly when communication matters most.
• Emergency links are narrowband. Satellite / HF–VHF channels carry a few hundred bits per second — not kilobits.
• Voice is 8–16 kbps, continuous. It physically cannot fit a few-hundred-bps link, however compressed.
• SMS fits — but context doesn't. Injuries, location, boat condition: in a crisis, people must speak, not type.
• Panic, noise, non-literate users. Speaking is the most inclusive, natural interface — if the link can carry it.
REAL-WORLD EXAMPLE
A fisher off the Konkan coast: one crewman injured, boat taking on water. Cellular is dead; a voice call is impossible over the low-rate link. SMS can't say “third man — arm bleed — leaking fast” — and nobody can answer by voice.
The hidden trap: the phone “always works” — until it is the only thing that doesn't. The last mile of crisis communication is a link too thin for audio.

## Slide 3
WHY SANWAD IS DIFFERENT
50–100× less data than audio — the same voice experience
Sanwad · PS 26173 · ISRO SAC · SIH 2026
03
Per 5-second utterance — same units, same window:
~100 B
Sanwad: one sentence as text
40–80 KB
raw voice at 8–16 kbps
50–100×
less data crosses the link
Text-first, voice-at-both-ends.
The phone speaks at both ends — STT turns speech into text, TTS turns it back — but only ~100 B of text crosses the link. That one decision is why the same app runs over Wi-Fi Direct / Bluetooth today, and ports to LoRa, NavIC-ecosystem messaging and HF/VHF packet links later — no re-architecture.
vs. existing walkie-talkie apps: cellular-based (die with the network) or VHF radio hardware (new equipment). Sanwad is the phone you already carry.

## Slide 4
TECHNICAL APPROACH
How a word becomes a voice on the other phone
Sanwad · PS 26173 · ISRO SAC · SIH 2026
04
PHONE A · SPEAK → TEXT
Mic + VAD
pause & stoppage detection
On-device STT
IndicConformer · 10 languages · int8 TFLite
Sentence JSON
≈ 100 bytes per sentence
Wi-Fi Direct / Bluetooth LE
TEXT ONLY — AUDIO NEVER CROSSES
PHONE B · TEXT → SPEAK
Local TTS
per-language model, on-device
Normal message
played back as a voice note
Alert message
highest volume · non-interruptible · bypasses mute
Push-to-talk walkie-talkie UI · same app on both phones · behaves like a normal phone when the mode is off

## Slide 5
TECHNOLOGY CHOICES
What we build with — and what we rejected
Sanwad · PS 26173 · ISRO SAC · SIH 2026
05
STT — SPEECH TO TEXT
• Primary: IndicConformer (AI4Bharat). TFLite int8, fully on-device, 10 languages.
• Fallback: Whisper.cpp. Broader accent robustness at a larger footprint.
• Evaluated, not selected: Vosk. Indic language coverage below this brief's bar.
• Design rule: STT fires on detected pause; emits one compact sentence at a time.
TTS — TEXT TO SPEECH
• Baseline, all 10 languages: espeak-ng. Fully offline, tiny, fast, intelligible.
• Neural where supported: Piper (en / hi). Better naturalness for high-frequency alert phrases.
• Priority: speed + intelligibility over studio fidelity — this is emergency comms.
• Alerts: highest volume, non-interruptible playback, bypasses system mute.
100% OFFLINE
no cloud, no cellular
OPEN SOURCE ONLY
Apache-2.0 / MIT · license audit in progress
2 GB RAM TARGET
₹8–10k · Cortex-A53-class devices

## Slide 6
AGAINST THE EVALUATION RUBRIC
Efficiency · Accuracy · Latency — targets we can prove
Sanwad · PS 26173 · ISRO SAC · SIH 2026
06
EFFICIENCY
20%
• STT model < 300 MB int8, on-device
• App footprint < 500 MB installed
• Memory 2 GB RAM target
• Idle listening < 5% CPU (VAD-gated decode)
• Operating cost ₹0 recurring cloud / cellular
ACCURACY
40%
• STT WER target on in-domain test set, all 10 languages
• TTS human legibility + flow panel
• Safety net text preview before playback — errors visible, fixable
• Tuning loop fine-tune / swap model per language if WER misses
LATENCY
20%
STT — pause detect + decode
1.5–2.5 s
Transport — Wi-Fi Direct / BLE
< 0.5 s
TTS — synthesize + start
< 1.5 s
Mouth-to-ear total
≤ 4–5 s
RTF target < 0.5 · measured on target device
Honest note: these are design targets, not measurements. Benchmarking is planned on a ₹8–10k device; we will present measured numbers at demo time.

## Slide 7
ROADMAP & ADOPTION
From a two-phone demo to a district-scale service
Sanwad · PS 26173 · ISRO SAC · SIH 2026
07
PHASE 1 · NOW (SIH)
Complete Android app. Live walkie-talkie demo: two phones over Wi-Fi Direct / Bluetooth, STT→TTS in 10 languages, with an on-screen packet log proving only text crosses the link.
PHASE 2 · FIELD
LoRa bridge for mesh relay. Low-rate messaging study (NavIC-ecosystem / HF–VHF packet). Pilots with NDRF and state maritime boards.
PHASE 3 · SCALE
B2G distribution with district administrations (DPI). Multilingual alert library. Per-language model updates.
Target adoption path (hypothesis to test, not assumption): NDRF → state maritime boards → district administrations (DPI). Pilots in negotiation.
We ask ISRO: guidance on low-rate messaging specs (bit budget, update interval) and support for a field pilot.
Zero recurring cloud or cellular cost. Words travel even when data can't.